Command	Transmitted(ASCII)	Received(ASCII)
ACV	syst:math:chan 0 / calc:stat 0 / conf:volt:ac / sens:det:band?	+003
DCV	syst:math:chan 0 / calc:stat 0 / conf:volt:dc / sens:det:rate?	SLOW
ACI	syst:math:chan 0 / CALC:FUNC OFF,REL / CALC:FUNC OFF,HOLD / CALC:FUNC OFF,MAX / conf:curr:ac / sens:det:band? / Sens:det:band?	+003
DCI	syst:math:chan 0 / CALC:FUNC OFF,REL / CALC:FUNC OFF,HOLD / CALC:FUNC OFF,MAX / conf:curr:dc / sens:det:rate? / sens:det:rate?	SLOW
2/4W (2W single press)	syst:math:chan 0 / conf:res / sens:det:rate?	SLOW
2/4W(4W double press)	syst:math:chan 0 / CALC:FUNC OFF,REL / CALC:FUNC OFF,HOLD / CALC:FUNC OFF,MAX / conf:fres / sens:det:rate?	SLOW
DIODE	syst:math:chan 0 / conf:diod / sens:det:rate?	SLOW
CONTINUITY (diode double press	syst:math:chan 0 / conf:cont / sens:det:rate?	SLOW
Hz/P (frequency: single press)	syst:math:chan 0 / conf:freq / sens:FREQ:APER? / sens:FREQ:APER?	+1.00E-1
Hz/P (period: double press)	syst:math:chan 0 / CALC:FUNC: OFF,REL / CALC:FUNC: OFF,HOLD / CALC:FUNC: OFF,MAX / conf:per / sens:FREQ:APER? / sens:FREQ:APER?	+1.00E-1
TEMP (Celsius: single press)	syst:math:chan 0 / SENS:TEMP:TCO:TYPE? / CONF:TEMP:TCO J / unit c / sens:det:rate?	SLOW
TEMP (Fahrenheit: double press)	syst:math:chan 0 / SENS:TEMP:TCO:TYPE? / CONF:TEMP:TCO J / unit f / sens:det:rate?	SLOW
AUTO	//first press will send the current mode cmds again / //second press / syst:math:chan 0 / conf:auto off / sens:det:rate?	SLOW
Range UP/DOWN	Send standard voltage current cmd / append ‘conf:curr:ac’ with either 0.001, 0.01, 0.1, 1, 10. can use 0.0001 for DC measurement. / For ac voltage can use one of the following: 0.1, 1, 10, 100 or 750. for DC voltage use: 0.1, 1, 10, 100, 1000.	//repeats mode output on every button press.
HOLD(on: single press)	syst:math:chan 0 / calc:func hold / calc:hold:ref? / sens:det:band?	SLOW
HOLD(change percentage: use range buttons)	syst:math:chan 0 / CALC:HOLD:REF? / calc:hold:ref 0.01 / calc:func hold / calc:hold:ref? / sens:det:band? / Can send: 0.01, 0.1, 1 and 10	SLOW
HOLD(off:double press)	syst:math:chan 0 / calc:func off / sens:det:rate?	SLOW
TRIG	syst:math:chan 0 / sens:det:band?	SLOW
2ND(same on each press)	syst:math:chan 0 / sens:det:band?	SLOW

Advanced measurement commands:	Transmitted data(ASCII)	Received data(ASCII)
REL	syst:math:chan 0 / val1?	-0.4E -8,A DC,+0001# //no space after E
dbm(shift & diode)	syst:math:chan 0 / sens:det:band?	SLOW
db(shift & Hz/P)	syst:math:chan 0 / sens:det:band?	SLOW
MX/MN (max: single press)	syst:math:chan 0 / calc:func max / sens:det:band?	SLOW
MX/MN (min double press)	syst:math:chan 0 / calc:func min / sens:det:band?	SLOW
compare(shift & hold)	//will ask you to set upper limit, i assume you must press enter / syst:math:chan 0 / calc:lim:upp? / sens:det:rate? / //once enter has been pressed / syst:math:chan 0 / calc:lim:upp 1 //1 is the value? / calc:lim:low? / //enter pressed again / syst:math:chan 0 / calc:lim:low -1 //this set value / calc:func comp / //shift hold to exit / calc:stat 0 / sens:det:rate?	SLOW00000E+0 / -1.000000E+0

Logging data	Transmitted data(ASCII)	Received data(ASCII)
Appears to be the same for all modes	SENS:ZERO:AUTO ON / SENS:GAIN:AUTO ON / SYST:DISP ON / TRIG: DEL 10 / read? buf / read? buf / read? buf / read? buf / read? buf / read? buf / read? buf / read? buf / read? buf / //continue at whatever frequency needed / read? buf / read? buf / read? buf / read? buf / sens:det:band? / SYST:LOC / //NB for AC measurement use: ‘sens:det:band? For DC use: ‘sens:det:rate?’	//data format / +0031660E-2, +0.0E+0 / //for dc, will return slow at end